## Slide 2: Did you know, that…
… viadonau takes charge of 250 kilometres of asphalted cycle tracks?
… the flood protection facilities
between Vienna and the
Slovakian border protect more than 600,000 inhabitants?
… viadonau locks through more than
90,000 vessels per year?
… viadonau ensures the preservation of 500 kilometres of towpaths?
… viadonau cares for 800 kilometres
of riverbank?
… between 9 and 12 million tons of goods are transported every year on the Austrian stretch of the Danube?
… viadonau manages 300 kilometres of flood protections facilities?
… viadonau manages 15,000 hectares of real estate?
… over 300 bird species are native along the river Danube?
… one inland vessel transports a ton of goods 4 times further than a truck, but with the same expenditure of energy?

## Slide 3: Flood Management Activities of viadonau
Bad Deutsch-Altenburg, 14. November 2017

## Slide 4: Agenda
  Overview
  Department of Flood Management - Duties and Responsibilities
  Flood Emergency Response and Management
  Rehabilitation of Flood Protection Facilities

## Slide 5: Overview

## Slide 6
Have a look at our logistics centre. Directly connected to over 80 million costumers.

## Slide 7: This is why 260 employees work along the riverbank of the Danube …

## Slide 11: … at the locks…

## Slide 15: … on board of vessels …

## Slide 17: and in the four service centres Oberes Donautal, Wachau, Carnuntum and March/Thaya as well as in the head office in Vienna.

## Slide 18: Available for you on 378 kilometres.
via donau – Österreichische Wasserstraßen-Gesellschaft mbH
company owner: Ministry of Transport, Innovation and Technology
founded 2005
about 260 employees
Turnover 2016: ca. 30 million Euros
Notes: Bild in Englisch !!!

## Slide 19: Corporate Objectives - four business pillars

## Slide 20: Department of Flood Management Duties and Responsibilities

## Slide 21: Flood protection
Goal:
Ensuring flood protection

## Slide 22: Water protection
Goal:
Preservation and improvement of the eco-systems Danube, Morava and Thaya

## Slide 23: Department of Flood Management
Flood protection operations
  Implementation of protective and preventive measures for the safe discharge of flood water
  Prevention of flood damage
  Flood emergency response and management
Flood protection projects
  Rehabilitation of flood protection facilities

## Slide 24: Flood protection operations
Dry weather operations
Day-to-day operation of the flood protection facilities
    Maintenance
    Regular inspections
    Functionality tests
    Safety checks

## Slide 25: Flood protection operations
Flood emergency response and management
Monitoring of river water levels
Flood emergency response in cooperation with local authorities and emergency services

## Slide 26: Flood protection operations
 | Morava and lower Thaya region | Danube region
Client | viadonau is contracted by 2 Flood Protection Associations | Danube Flood Control Agency (bmvit, City of Vienna, Federal State of Lower Austria)
River | Morava Lower Thaya | Danube (in lower Austria and Vienna including the tributaries influenced by the backwater of the Danube)
Flood protection facilities | approx. 75 km | approx. 300 km (observed during flood events: approx. 162 km)
Objects | 65 culverts, sluices and other structures (pumping stations, mobile flood defense systems, …) (65 operated during flood events) | 13 bridges 90 culverts, sluices and other structures (pumping stations, mobile flood defense systems, …) (55 operated during flood events)

## Slide 27: Flood protection operations
 | Morava and lower Thaya region | Danube region
Dry Weather Operations | Coordination Supervision The day-to-day operation of the flood protection facilities is carried out by the Flood Protection Associations | Day-to-day operation of the flood protection facilities Maintenance Regular inspections Functionality tests Safety checks
Flood Emergency Response | Coordination Supervision Guard duty and defensive measures are carried out by the local voluntary fire brigade | Guard duty Defensive measures Supported by local voluntary fire brigade and federal armed forces
 | 4 persons active during flood emergency response | 40 persons active during flood emergency response

## Slide 28: Flood Emergency Response and Management

## Slide 29: Flood emergency response
Organisation
Managing Director viadonau
Head of Flood Emergency Response
Head of Outpost
Head of Outpost
Hydrologist
Guard I
Guard II
Guard I
Guard II
Head of Outpost
Guard I
Guard II

## Slide 30: Flood protection operations
Krems
Stockerau
Nußdorf
viadonau headquaters
Albern
Wehr 2
Orth
Bad Deutsch-Altenburg
Hainburg
Markthof
Angern
Danube: 9 outposts
Morava: 1 outpost

## Slide 31: Flood emergency response
Monitoring and Alerting
  9 published gauges on the Danube
  current water level
  deviation to last measurement
  low-water forecast : 5 days
  published flood forecasting: 2 days (calculated: ~ 3 days)

## Slide 32: Flood emergency response
Reference gauge for Danube:
KIENSTOCK

## Slide 33: Flood emergency response
Stage Model
  Flood emergency response depending on water level at reference gauge
  The beginning of a stage is defined by the exceedance of a specific water level at reference gauges (upward trend)
  Staff schedule for each stage
  4 Stages
  Early warning stage
  Alert
  Flood Emergency Response Stage I
  Flood Emergency Response Stage II

## Slide 34: Flood emergency response
Dry weather operations
Dry weather operations
Flood emergency response
Early Warning Stage
Alert
Flood Emergency Response
Stage I
Flood Emergency Response
Stage I
Flood Emergency Response
Stage II
Water level
at reference gauge
500cm
KIEN
650cm
KIEN
750cm
KIEN
850cm
KIEN
900cm
KIEN
800cm
KIEN
700cm
KIEN
Alert
Cleanup
Time

## Slide 35: Flood emergency response
Early Warning Stage
  The beginning and end of the early warning stage are determined by the hydrologist on-duty and the head of flood emergency response based on:
    Weather forecast
    Current water level / Water level forecast
  If necessary: Initiation of on-call duty for staff for next stage
  Activities:
  Monitoring of water levels, weather forecast and water level forecast by the Hydrologist on-duty
  Coordination between Hydrologist on-duty and Head of Flood Emergency Response

## Slide 36: Flood emergency response
Alert
  The beginning and end of the Alert stage are determined by Managing Director of viadonau based on:
    Current water level / Water level forecast
  If necessary: Initiation of on-call duty for staff for next stage
  Activities:
  Monitoring of water levels, weather forecast and water level forecast by the Hydrologist on-duty
  Coordination between Hydrologist on-duty and Head of Flood Emergency Response
  Functionality of flood protection facilities are controlled once a day

## Slide 37: Flood emergency response
Flood Emergency Response Stage I
  The beginning and end of the Alert stage are determined by Managing Director of viadonau based on:
    Current water level / Water level forecast
  Managing Director informs bmvit & Danube Flood Control Agency
  If necessary: Initiation of on-call duty for staff for next stage
  Activities:
  Monitoring of water levels, weather forecast and water level forecast by the Hydrologist on-duty
  Coordination between Hydrologist on-duty, Head of Flood Emergency Response, Head of Department of Flood Management
  Out-Post: Head of outpost and 1 staff (daily 07:30 – 17:30)
    Inspections of all facilities once a day
    Reading of manual gauges once a day

## Slide 38: Flood emergency response
Flood Emergency Response Stage II
  The beginning and end of the Alert stage are determined by Managing Director of viadonau based on:
    Current water level / Water level forecast
  Managing Director informs bmvit & Danube Flood Control Agency
  Activities:
  Establishment of crisis unit (daily 07:30 – 17:30, on-call duty at night)
  Monitoring of water levels, weather forecast and water level forecast by the Hydrologist on-duty (daily 06:00 – 22:00, on-call duty 22:00 – 06:00)
  Out-Post: Head of outpost and up to 4 staff (daily 00:00 – 24:00)
    Inspections of all facilities at least once a day
    Inspections of areas where water levels reach the facilities at least twice a day
    Reading of manual gauges three times a day

## Slide 39: Flood emergency response
EARLY WARNING STAGE
ALERT
FLOOD EMERGENCY RESPONSE
STAGE I & II
WATER LEVEL KIENSTOCK (REFERENCE GAUGE)
INITIATION OF FLOOD EMERGENCY RESPONSE STAGE
ALERT
Flood Event June 2013 (HQ300)

## Slide 40: Flood emergency response
Defensive Measures
Sandbags
Mobile flood defense systems
Supported by local voluntary fire brigade and federal armed forces

## Slide 41: Flood emergency response
 | “Normal operation” (in case of a flood) | Disaster
Responsibility | viadonau | Local authorities
Water level | Water level below design water level | Water level above design water level (HQ100)
Functional capability of flood protection facility | Facility is fully functional | Failure of essential facility component (i.e. dike breach)
Operation | Operator is able to control the situation with own forces | Additional forces required
On duty | viadonau Local voluntary fire brigade (upon request of operator) Experts upon request of viadonau (i.e. geotechnical) | Local authorities viadonau Local voluntary fire brigade (upon request of local authorities) Authorised experts Federal armed forces

## Slide 42: Terminology
Level of design discharge Design water level
Impermeable layer (clay)
Aquifer
MW
Dike crest
Maintenance path
Berm
Freeboard
water-side dike toe
land-side dike toe
Dike

## Slide 43: Drainage by surcharge
apply geomambrane
charge with permeable filling material
  Goal: no sediment (fine material) erosion, no slope failure, dike remains structually stable

## Slide 44: Drainage by surcharge
WSP
Aquifer
soaked dike with seepage surface line
rising groundwater
possible slip circle
apply geomembrane
apply sandbags first of all at the land-side dike toe
Impermeable layer (clay)
do not avoid water outlet !

## Slide 54: Rehabilitation of Flood Protection Facilities

## Slide 55: Failure mechanisms of dikes
Most common failures of dikes
Impact on dikes
Overtopping
Seepage
Undercurrent
Static water pressure
Wave impact, ice impact in winter
Overtopping
Seepage/Undercurrent
Slope failure
Erosion
Subsurface erosion

## Slide 56: Failure mechanisms of dikes

## Slide 57: Failure mechanisms of dikes

## Slide 58: Failure mechanisms of dikes

## Slide 59: Rehabilitation measures
Technical measures to prevent damages/failures
  Individual technical measures or combination of various measures
  Implementation during construction of dike
  Subsequent incorporation during rehabilitation of dike
  Goal: Improvement of functionality and structural stability

## Slide 60: Construction process
  Removal of the existing embankment
  Removal of the existing embankment in short sections

## Slide 61: Construction process
Construction of new embankment
  The new embankment is built up in compacted layers
  Slopes are covered by a humus layer and re-cultivated

## Slide 62: Drainage elements at base of the dike
  Seeapage of water through the dike; during longer impoundment a seepage line is developed
  Seepage line is releasing pressure in the drainage element, seepage water can exit at the base of the dike
  No sediment (fine material) erosion, no slope failure, dike remains structually stable
WL
Impermeable layer (clay)
Aquifer
Drainage element

## Slide 63: Drainage elements at base of the dike

## Slide 64: Internal sealing
  Seepage of water through the dike
  Sealing (i.e. Diaphragm wall, Mixed-in-place wall, sheet piling) prevents further seapage
  Seepage path is lengtened due to sealing, quantity of seaapage water is reduced
  No slope failure, dike remains structually stable
Impermeable layer (clay)
Aquifer
Sealing
WL

## Slide 65: Construction process
Diaphragm wall
  Only sealing function
  Static function performed by the dike embankment
  I-beam is vibrated into the ground; as the beam is withdrawn, the resulting cavity is filled with betonite slurry
  Thickness approx. 8-12 cm

## Slide 66: Construction process
Mixed-in-Place wall
  Sealing function
  Partial static function (main static function performed by the dike embankment)
  Spiral is rotated into the ground, the soil is rearranged and the cavities are filled with suspension
  Thickness: 40-50 cm

## Slide 67: Pressure relief drainage
  Aquifer is recharged by groundwater and infiltrating surface water
  Uplift pressure is relieved by gravel pillars
  Dike remains structually stable
Pressure relief draiage
WL
Impermeable layer (clay)
Aquifer

## Slide 68: Construction process
Gravel pillars for relief drainage
  Drainage effect achieved by gravel pillars wrapped in fleece
  Method: drilling or pile-driven

## Slide 69: Superimposed load filling
  Aquifer is recharged by groundwater and infiltrating surface water
  Weight of the superimposed load filling counteracts the uplift pressure of the groundwater
  Dike remains structually stable
WL
Superimposed load filling
Impermeable layer (clay)
Aquifer

## Slide 70: Construction process
Maintenance path
  3m wide path
  usually built at the land-side dike toe
  in exceptional cases built along the dike crest
  for maintenance and
  to provide access to the dike in case of flooding (defensive measures)

## Slide 71: Construction process
Surface of dike crest
  Gravel path
  Asphalt (cycle path)

## Slide 72: Construction process
HW 100
Impermeable layer (clay)
Gravel pillars for pressure relief drainage at the dike base
Diaphragm wall/Mixed-in-Place wall
Removal of the existing dike crest
If necessary: removal of the existing dike; new dike is built up in compacted layers to the level of design discharge
Permeable filling material
Dike crest
Maintenance path
Aquifer

## Slide 73: Flood protection projects
 | Morava and lower Thaya | Danube
Client | Flood Protection Associations | Danube Flood Control Agency
Financing | bmvit, Federal state of Lower Austria, municipalities | bmvit, City of Vienna, Federal State of Lower Austria
Investment | approx. € 123 Mio. | approx. € 95.4 Mio.
Length | approx. 80 km | approx. 67 km
Protected population | approx. 18.000 individuals (in 10 municipalities) | approx. 30.000 individuals (in 12 municipalities)
Design discharge | HQ100 + 70 cm freeboard | > HQ1000 (Q = 14.000 m3/s) + variable freeboard (0 – 50 cm)
Construction measures | Sealing: Diaphragm wall Relief drainage: Gravel pillars Protective strip surface: gravel Dike crest surface: gravel | Sealing: Mixed-in-Place wall Relief drainage: Gravel pillars Protective strip surface: grass Dike crest and maintanance path surface: gravel or asphalt (cycle track)
Construction period | 2006 – 2012 | 2017 - 2020

## Slide 74: Rehabilitation of Flood Protection along the River Danube east of Vienna

## Slide 75: Background
  Provides flood protection for City of Vienna and for parts of Lower Austria east of Vienna
  Design discharge: 14.000 m3/s (>HQ1000)
  Construction of dike 120 years ago
  Last rehabilitation in 1970ies (only certain sections of the dike)
  Defensive measures during flood events (2002, 2013)
  2d model: raising dike crest level necessary

## Slide 76: Flood protection system

## Slide 77: Flood protection system
Video

## Slide 81: Challenges
  Permits
    Water law
    Conservation law
    National park law
    Forest law
  Trans-border-system
  Protected area (national park, Natura-2000, nature reserve, landscape conservation area)
  Conflicting interests (agriculture, nature conservation, tourism)

## Slide 82: Trans-border system
PHHQ 14.000 m³/s
PHHQ 14.000 m³/s
1.080 m³/s
720 m³/s
13.200 m³/s
13.420 m³/s
800 m³/s
540 m³/s
280 m³/s
140 m³/s
Morava (HQ30)
1.040 m³/s
SK
13.200 m³/s
13.150 m³/s
12.920 m³/s
13.280 m³/s
Discharge as per consent 1977
Discharge as per 2D-model
Overflow section
Overflow starts at 12.000 m³/s

## Slide 83: Environment protection
  National park

## Slide 84: Environment protection
  Natura 2000 is a network of nature protection areas in the territory of the European Union.
  It is made up of Special Areas of Conservation (SACs) and Special Protection Areas (SPAs) designated respectively under the Habitats Directive and Birds Directive.

## Slide 85: Objects of protection
  Dry grassland
  Orchids
  Amphibians
  Reptiles
  Birds

## Slide 86: Dry grassland
  Precious dry grass lands
  Red-listed species
  Habitat for snail, grasshopper, butterfly

## Slide 87: Orchids
Red-listed species
  Orchis militaris
  Anacamptis morio
  Neottinea ustulata

## Slide 88: Butterflies

## Slide 89: Dry grassland & Orchids

## Slide 90: Orchids
  Measures
  Manual relocation of orchids

## Slide 91: Forest
Measures
  Preservation of precious trees
  compensatory measures (i.e. forestation)

## Slide 92: Amphibians and reptiles
  Reptiles use dike as wintering grounds
  Amphibians cross the dike to get to water bodies

## Slide 93: Amphibians and reptiles
Measures
  mobile seasonal fences for amphibians
  Amphibians are caught in buckets, transferred by hand to other side of the dike

## Slide 94: European pond terrapin
  Red-listed species
  Without measures construction only possible one month per year due to reproduction cycle

## Slide 95: European pond terrapin
Measures
  Construction ban during egg deposition (15.5.-15.7.)
  3 types of protective measures: artificial hatching, cages, fences

## Slide 96: Birds
  sea eagle
  black stork
  honey buzzard
Measures
  Identification of nests
  Construction ban during sensitive periods of reproduction

## Slide 97: Seeds
Measures
  seeds are collected along the dike by hand
  Re-cultivation of slopes with seeds that are adapted to the situation

## Slide 98: Thank you for your attention!
Contact
Stefan Scheuringer Head of Flood Management T +43 50 4321-2603 stefan.scheuringer@viadonau.org Donau-City-Straße 1
1220 Vienna